## Slide 1: Telink Semiconductor BT Audio AEC & NS
2017.07

## Slide 2
Echo cancellation performance
Moderate SNR(10dB) and echo tail length(128ms). Without residual echo suppression ERLE is 20-30dB; With residual echo suppression ERLE seems better than 40dB.
Noise suppression performance
The noise can be suppressed by adjusting the gain floor(-15dB).

## Slide 3: Echo Cancellation
Echo tail length:
LMS->Frequency LMS(FLMS)->Multi-delay block Frequency LMS(MDF)
Example: Sampling Rate 8KHz; Echo tail length is 128ms(1024 points); Frame size is 16ms(128 points).
MDF scheme: N is frame size 128 points; Delay block number is 16; Equivalent tail length is 128*16=1024 points.
Adapted rate:
Sub-band, Normalization(time or frequency domain), pre-emphasis filter
VAD:
Coherence(coherence between microphone and far-end speech), two-path logic, Step size control
Scheme: MDF + Normalization & Pre-emphasis filter + Two-path logic & Step size control

## Slide 5: Noise Suppression
Noise estimation
When to update? Voice activity detection at every frequency point.
Posteriori & priori SNR estimation
Posteriori SNR is estimated every frame, priori SNR is smoothing result
Speech presence probability estimation
stable process
Gain estimation
log MMSE

## Slide 7: Simulation result
Case 1: SNR = 0dB, echo tail length = 128ms

## Slide 8: Simulation result
Case 2: SNR = 10dB, echo tail length = 128ms

## Slide 9: Simulation result
Case 3: SNR = 10dB, echo tail length = 128ms