Echo cancellation

By ZhengChen

Change Log
Version	Description	Author	Date
0	Initial version	Z.C	17／7／11

       Figure 1: Echo cancellation flowchart

     Figure 2: Two-path algorithm

Definitions

N: frame size
M:delay blocks
Sff: foreground filter error variance
Sbb: background filter error variance
Sxx: far-end speech variance
Sdd: microphone signal variance
Davg1, Davg2, Dvar1, Dvar2 : parameters for update foreground filter/ reset background filter

## Initialization Parameters
1. Pre-process:
  DC_mem(0) = DC_mem(1) = 0 newline Emp_mem(0) = Emp_mem(1) = 0
2. Foreground filter output
  X(m,j) = 0,~m=0,1,...,M newline xTemp(n) = 0, ~n=0,1,...,2N-1 newline W_fore(m,j) = 0,~m=0,1,...,M-1
3. Proportional rate update
  Ratio of 10 between adaption rate of the first and last block.
  decay = e^{- {2.4 over M}} newline adaptivePropTemp(0) = 0.7 newline adaptivePropTemp(m) = adaptivePropTemp(m-1)*decay, ~ m=1,2,...,M-1 newline adaptiveProp(m) = {0.8 adaptivePropTemp(m)} over sum from{m=0} to{M-1} {adaptivePropTemp(m)}
4. Background filter upadte:
  e_fore(n,j) = 0,~n=0,1,...,N-1 newline adaptivePower_-1(k,j) = 1,~k=0,1,...,N newline W_back(m,j) = 0,~m=0,1,...,M-1
5. Backgrounf filter output

1. Update foreground filter or reset background filter
  Davg1(j) = Davg2(j) = Dvar1(j) = Dvar2(j) =0
2. AEC output
  DeEmp_mem = 0 newline screwedUpCnt = 0
1. Adaptive filter Convergence decision
  adaptiveCon = 0 newline adaptiveSum = 0 newline leakageEsti = 0
2. Learning Rate
        daptivePower(k,j) = 0,~k=0,1,...,N newline Eh(k,j) = Yh(k,j) = 0,~k=0,1,...,N
## Pre-process
1. Microphone signal is applied with DC notch filter and pre-emphasis filter. Far-end speech is only applied with pre-emphasis filter.
2. DC notch filter: A 2-st order IIR filter with configured coefficients, dicided by sampling rate. For typical sampling rate 8Ksym/s, the related coefficients are:
  Numerator: [1 -2 1]. Denominator:[1 -1.62 0.7353]. Gain: 0.9
  H(z) = {Y(z)} over{X(z)} = {0.9-1.8z^{-1}+0.9z^{-2}}over{1-1.62z^{-1}+0.7353z^{-2}}
  The DC notch filter process is as follows:
  d_{DC~temp} = d_orignal(n,j)-DC_mem[0] newline newline DC_mem[0] = DC_mem[1]-2 d_orignal(n,j)+1.8 d_{DC~temp} newline newline DC_mem[1] = d_orignal(n,j)-0.817d_{DC~temp} newline newline d_DC(n,j) = 0.9 d_{DC~temp}
  The filter frequency domain response is as follows:
3. Pre-emphasis filter: A FIR filter with coefficients: [1 -0.9].
  For microphone signal:
  d(n,j)=d_DC(0,j)-0.9 Emp_mem(0) newline newline d(n,j) = d_DC(n,j)-d_DC(n-1,j),~n=1,2,...,N-1 newline newline Emp_mem(0) = d_DC(N-1,j) newline newline Sdd = sum from{n=0}to{N-1} {abs{d(n,j)}}^2
  For far-end speech:
  x(0,j)=x_orignal(0,j)-0.9 Emp_mem(1) newline newline x(n,j) = x_orignal(n,j)-x_orignal(n-1,j),~n=1,2,...,N-1 newline newline Emp_mem(1) = x_orignal(N-1,j) newline newline Sxx=sum from{n=0} to{N-1} {abs{x(n,j)}}^2
The frequency domain response is as follows:

## Foreground filter output
1. Use MDF algorithm to calculate the estimated echo for foreground, then get error and related variance.
2. Sff is used to decide if to update the foreground filter or reset the background filter.

       X(m+1,j) = X(m,j), m=0,1,...,M newline newline xTemp(0:2N-1)=[xTemp(N:2N-1),~ x_0(j),...,x_{N-1}(j)] newline newline X(0,j) = FFT(xTemp) newline newline y_fore(n,j) = last N terms of lbrace IFFT[sum from{m=1} to {M} {X(m,j)W_fore(m,j)}] rbrace,~n=0,1,...,N-1 newline newline e_fore(n,j) = d(n,j)-y_fore(n,j),~n=0,1,...,N-1 newline newline Sff = sum from{n=0} to{N-1} {abs{e_fore(n,j)}}^2

## Proportional rate update
1. If the filter has convergenced, i.e adaptiveCon = 0 . Use the initial proportional rate.
2. If the adaptive has convergenced, i.e adaptiveCon = 1 . The update process is as follows:
  W_{backSum}(m,j)= sqrt{1.0+sum from{n=0}to {N-1} {abs{W_{back~n}(m,j)}}^2},~m=0,1,...,M-1 newline newline maxW_{backSum} = MAX(W_{bakcSum}) newline newline W'_{backSum}(m,j) = W_{backSum}(m,j)+0.1 maxW_{backSum} newline newline adaptiveProp(m,j) = {0.99 W'_{backSum}(m,j)} over {1.0+sum from{m=0}to{M-1}{W'_{backSum}(m,j)}}

## Background filter update
1. The cofficients of background filter can be updated by MDF or AUMDF algorithm.
2. For AUMDF algorithm, the final step is only applied for m=0 or other case.
        E(j) = FFT [ 0,...,0,e_{fore~0}(j),...,e_{fore~N-1}(j) ] newline newline u_optimal(k,j) = adaptiveProp(k,j)*adaptive Power_-1(k,j), ~n=0,1,...,N-1 newline newline W_back(m,j) = W_back(m,j-1)+u_optimal X^{*}(m+1,j)E(j),~m=0,...,M-1 newline newline W_{back temp}(m,j) = first N terms of lbrace IFFT[W_back(m,j)] rbrace,~(AUMDF:m=0; MDF:m=0,1,...,M-1) newline newline W_back(m,j) = FFT[W_{back ``temp}(m,j),0,...,0]

## Background filter output
Sbb and Dbf is used to decide if update the foreground filter or reset background filter.

        y_back(n,j) = last N terms of {IFFT[sum from{m=1} to {M} {X(m,j)W_back(m,j)}]},~n=0,1,...,N-1 newline newline e_back(n,j) = d(n,j)-y_back(n,j),~n=0,1,...,N-1 newline newline Sbb = sum from{n=0} to{N-1} {abs{e_back(n,j)}}^2 newline newline Dbf = sum from{n=0} to{N-1}{abs{e_back(n,j)-e_fore(n,j)}}^2

## Update foreground filter or reset background filter

  1. Parameters should be calculated every frame for the decision are as follows:

        Davg1(j) = 0.6*Davg1(j-1)+0.4*(Sff-Sbb) newline newline Davg2(j) = 0.85*Davg2(j-1)+0.15*(Sff-Sbb) newline newline Dvar1(j)=0.36*Dvar1(j-1)+0.16*Sff*Dbf newline newline Dvar2(j)=0.7225*Dvar2(j-1)+0.0225*Sff*Dbf

The conditions to decide if to update foreground filter by background filter are any one of three as follows. Recommended foreUpdateVar1 is 0.5, foreUpdateVar2 is 0.25.

(Sff-Sbb)*abs{Sff-Sbb}>Sff*Dbf newline newline Davg1(j)*abs{Davg1(j)}>foreUpdateVar1*Dvar1(j) newline newline Davg2(j)*abs{Dvag2(j)}>foreUpdateVar2*Dvar2(j)
If satisfied, then
W_fore(k,j) = W_back(k,j),~k=0,1,...,N newline newline Davg1(j) = Davg2(j) = Dvar1(j) = Dvar2(j) = 0 newline newline y_fore(n,j) = win(n)*y_fore(n,j)+win(N+n)*y_back(n,j),~n=0,1,...,N-1 newline newline e_fore(n,j) = d(n,j)-y_fore(n,j),~n=0,1,...,N-1
The smooth window is hanning window
win(n) = 0.5-0.5cos(%pi n/N), ~ n=0,1,2,...,2N-1
1. If the foreground filter update condition are all not satisfied, decide if to reset the background filter by foreground filter. Recommended backResetVar is 4.0.
  -(Sff-Sbb)*abs{Sff-Sbb}>backResetVar*Sff*Dbf newline newline -Davg1(j)*abs{Davg1(j)}>backResetVar*Dvar1(j) newline newline -Davg2(j)*abs{Dvag2(j)}>backResetVar*Dvar2(j)
  if satisfied, then
  W_back(k,j) = W_fore(k,j),~k=0,1,...,N newline newline Davg1(j) = Davg2(j) = Dvar1(j) = Dvar2(j) = 0 newline newline y_back(n,j) = y_fore(n,j),~n=0,1,...,N-1 newline newline Sbb = Sff
## AEC output
Generally, get the output by applying the filter foreground error with de-emphasis filter.
out(0,j) = 0.9 DeEmp_mem+e_fore(0,j) newline newline out(n,j) = 0.9out(n-1,j)+e_fore(n,j),~n=1,2,...,N-1 newline newline DeEmp_mem=out(N-1,j)
## Reset Parameters
The pesudocode for the reset logic is as follows:
if (!(Sxx>0&&Syy>0&&See>0)||!(Sxx<N*2e9&&Syy<N*2e9&&Sff<N*2e9))
then [screwedUpCnt = screwedUpCnt+50]
elseif (Sff>Sdd+N*5000)
then [screwedUpCnt = scrwedUpCnt+1]
else
then [screwedUpCnt = 0]
end
if (screwedUpCnt > 50)
then [screwedUpCnt = 0; reset]
end

The reset parameters are as follows:

DC_mem(0)=DC_mem(1)=0 newline Emp_mem(0)=Emp_mem(1)=DeEmp_mem=0 newline W_fore(m,j) = W_back(m,j) = 0,~m=0,1,...,M=1 newline X(m,j) = 0,~m=0,1,...,M newline Davg1=Davg2=Dvar1=Dvar2=0 newline screwedUpCnt = 0 newline adaptiveCon = adaptiveSum = leakageEsti = 0 newline adaptivePower(k,j) = 0,~k=0,1,...,N newline adaptivePower_-1(k,j) = 1,~k=0,1,...,N newline newline Eh(k,j)=Yh(k,j)=0,~k=0,1,...,N
## Adaptive filter Covergence decision
The adaptive filter has covergenced once all of the three conditions satisfied:
adaptiveCon = 0 newline newline adaptiveSum > M newline newline leakageEsti > 0.03
if satisfied:
adaptiveCon = 1
## Learning Rate calculation
        Syy=sum from{n=0}to{N-1}{abs{y_fore(n,j)}}^2 newline newline Sey=sum from{n=0}to{N-1}{(y_fore(n,j)e_fore(n,j))} newline newline Yf(k,j) = first (N+1) terms of lbrace {abs{FFT[0,...,0,y_{fore~0}(j),...,y_{fore~N-1}(j)]}}^2 rbrace,~k=0,1,...,N newline newline Ef(k,j) = first (N+1) terms of lbrace {abs{FFT[0,...,0,e_fore(0,j),...,e_fore(N-1,j)]}}^2 rbrace,~k=0,1,...,N newline newline Xf(k,j) = first (N+1) terms of lbrace {abs{X(0,j)}}^2 rbrace,~k=0,1,...,N newline newline %gamma=0.35 over {M} newline newline adaptivePower(k,j)=(1-%gamma)adaptivePower(k,j)+%gamma Xf(k,j),~k=0,1,...,N

       Compute filtered spectra and (cross-)correlations:

     P_ey(k,j) = (Ef(k,j)-Eh(k,j))(Yf(k,j)-Yh(k,j)), ~k=0,1,...,N newline newline P_yy(k,j) = (Yf(k,j)-Yh(k,j))(Yf(k,j)-Yh(k,j)),~k=0,1,...,N newline newline %beta = N over Fs newline newline Eh(k,j) = (1-%beta)Eh(k,j)+%beta Ef(k,j),~k=0,1,...,N newline newline Yh(k,j) = (1-%beta)Yh(k,j)+%beta Yf(k,j),~k=0,1,...,N

        The (cross-)correlation recursively result are:

        P_{yy~ave} = sqrt{sum from{k=0}to{N}{P_yy(k,j)}} newline newline P_{ey~ave} = sum from{k=0}to{N}{P_ey(k,j)} over{P_{yy~ave}} newline newline %alpha = MIN(2N over{Fs} Syy over See,0.5N over{Fs}) newline newline R_ey=(1-%alpha)R_ey+%alpha P_{ey~ave} newline newline R_yy=(1-%alpha)R_yy+%alpha P_{yy~ave}

       Leakage estimation is:

        R_ey = MAX(R_ey,1) newline newline R_ey = MIN(R_ey,R_yy) newline newline leakageEsti = R_ey over R_yy

       Learning Rate estimation is:

        RER=(0.0001 Sxx+3 leakageEsti*Syy) over {See} newline newline RER=MIN(MAX(RER,Sey*Sey over {1+See*Syy}),0.5)

      If adptive filter has covergenced. i.e adaptiveCon = 1

        e(k,j) = Ef(k,j)+1, ~n=0,1,...,N newline newline r(k,j) = MIN(leakageEsti*Yf(k,j),0.5 e(k,j)),~k=0,1,...,N newline newline r'(k,j) = 0.7 r(k,j)+0.3 RER*e(k,j), ~k=0,1,...,N newline newline adaptivePower_-1(k,j) = {r'(k,j)} over {e(k,j)*(adaptivePower(k,j)+10)}
      If adaptive filter hasn't covergenced. i.e adaptiveCon = 0

        See = MAX(See,200 N) newline newline adaptiveRate = MIN({0.25 Sxx}over {See},0.25),~(if Sxx>2000 N satisfied) newline newline adaptivePower_-1(k,j) = adaptiveRate over {adaptivePower(k,j)+10}, ~k=0,1,...,N newline newline adaptiveSum = adaptiveSum+adaptiveRate

## Residual Echo Estimation
        If adptive filter has covergenced. i.e adaptiveCon = 1

        y_overlap(0:2N-1,j) = [y(N:2N-1,j), out(0,j), ... , out(N-1,j)] newline newline y_overlap'(n,j) = y_overlap(n,j)*window(n),~n=0,1,...,2N-1 newline newline Y_overlap(j) = FFT(y_overlap'(j)) newline newline echo_residual(k,j) = MIN(1,2*leakageEsti)*abs{Y_overlap(k,j)}^2 ,~k=0,1,...,N

        If adaptive filter hasn't covergenced. i.e adaptiveCon = 0

        y_overlap(n,j) = 0,~n=0,1,...,2N-1 newline newline echo_residual(k,j) = 0,~k=0,1,...,N